## Slide 1: Freifunk for Things
LoRaWAN & The Things Network
Freifunk Assembly, 33c3 Day2 -18:30

## Slide 2: Hello.

## Slide 3: Freifunk Mission
„Freifunk steht für freie Kommunikation in digitalen Datennetzen
Wir verstehen frei als öffentlich zugänglich, nicht kommerziell, im Besitz der Gemeinschaft und unzensiert.“

## Slide 4: LPWAN?
Low Power Wide Area Network
Notes: Low-Bandwith communication for autonomous devices
Low Energy Consumption
Batteries, Solar Cells, Energy Harvesting - Up to 10 years on a single battery
Long Range
kilometers!
means low infrastructure costs - “into the basement”
Low Cost & Simple
“Secure”
Non goal: High data rate

## Slide 5: Goals
Low-Bandwith communication for autonomous devices
Low Energy Consumption
  Batteries, Solar Cells, Energy Harvesting - Up to 10 years on a single battery
Long Range
  kilometers! -> means low infrastructure costs - “into the basement”
Low Cost & Simple
“Secure”
Non goal: High data rate

## Slide 6: IoT Applications
Yada yada: Wearables, Quantified Self, Smart* Home, Connected Car, “Locks”
Field is much wider, still emerging. #Neuland
I am interested in: Smart* Foo The world around us - based on Open Data. Let’s take stock!
*with variable definitions of „Smart“

## Slide 7: LPWAN & others
Quelle: F.Vannel, „Communications pour l’internet des objets“

## Slide 8: LPWAN ‘Standards’
Quelle: Nokia
(incomplete list)

## Slide 9: LPWAN is a compromise
Many restrictions
Receiver is mostly ‘off’
Rate limiting

## Slide 10: LoRaWAN Technology

## Slide 11: LoRa Radio
LoRa(tm) - a modulation
Unlicensed but regulated ISM bands
EU: 868 Mhz, US 913Mhz, 430 China,Japan
Chirp Spread Spectrum Modulation
  Demodulate ~20dBm below noise floor

## Slide 12: LoRa Chirp Spread Spectrum
See “Decoding the LoRa Phy” - Matt Knight
33C3, Day 3, Hall 6, 18:30
Notes: Spectacular link budget: demodulate at -134dBm

## Slide 13: 868 EU ISM Regulation
863-870 Mhz:
  <1% duty cycle
  25mW
Downlink channel (869,4-869,65)
  <10%
  500mW
863-865, 868,7-869,2: <0,1%

## Slide 14: Long Rang
ttnmapper.org
Long Range

## Slide 15: Enschede
ttnmapper.org
Friends
At
Enschede

## Slide 16: Range
~2-3 km urban
>10 km rural
> 100 km at freak conditions
Factors
  Line Of Sight (LOS)
  Elevation of Gateways
  Elevation of Node
  Be careful with nodes close to ground.

## Slide 17: LoRaWAN
LoRa® = Radio
LoRaWAN = Network
LoRa is SEMTECH proprietary LoRaWAN ist open specification
https://www.lora-alliance.org/

## Slide 18: LoRaWAN Structure
Notes: LoRa® = Radio
LoRaWAN = Network
LoRa is SEMTECH proprietary LoRaWAN ist open specification

## Slide 19: Basics
Gateways receive on all (8) channels (concurrently)
No overhead for coordination since there is none - “ALOHA network”
Gateways forward packets to network
Network is “just software”

## Slide 20: Device Classes
Class A
  Node transmits at will and waits a short time for a response
  No data reception outside ^^ recieve window
Class B
  Node listens at set intervals
  Synchronised via time beacons transmitted by Gateways
  Requires very precise time (µS) at Gateway and Node
Class C
  Node is constantly listening
  High energy consumption

## Slide 21: Power Consumption
e.g. MICROCHIP RN2483 (@3,3V)
  Transmit: 17-40 mA
  Receive: 14mA
  Idle: 2,8mA
  Deep Sleep: 9µA <<< Most of the time

## Slide 22: Payload
Captain Obvious: LoRaWAN is not TCP/IP
51..222 byte payload per message
Depending on data rate

## Slide 23: Adaptive Data Rate

## Slide 24: Why not a mesh?
Mesh requires too much energy
  Receiver needs to listen
  Active Link-State protocols require regular transmissions
Mesh collides with duty-cycle regulation

## Slide 25: Security
Mandatory AES128 crypto
Shared Secret between node and application
The verdict about the quality of this encryption (AES modes) is still out

## Slide 26: LoRaWAN Deployments
KPN, Netherlands
Proximus, Belgium
SK Telecom, Korea
Bouygues Telecom, France
Swisscom, Switzerland
telent, Germany

## Slide 28: The Things Network

## Slide 30: The Things Network
Crowd Sourced Network
Gateways owned by Individuals (swarm) & Organisations
Open Source LoRaWAN Network Stack
Run by „The Things Network Foundation“
Free as in free & free as in beer

## Slide 31: Communites

## Slide 32: Buy…
Kaufenoder bauen

## Slide 33: Or build your own
IMST LoRaWAN Concentrator: ~180€
Raspberry Pi + Open Source
#win
https://github.com/ttn-zh/ic880a-gateway/wiki

## Slide 34: Nodes
Build your own(RN2483, HopeRF) + MCU (e.g. Arduino)
Buy
  Sodaq Autonomo / One
  Moteino
  LoPy
  Adafruit Feather LoRa
  Lots of stuff in development
  Prices are coming down

## Slide 35: TTN API
Basic interface between app and network is MQTT
  RESTful management API
Web: https://staging.thethingsnetwork.org

## Slide 36: TTN in node.js
var ttn = require('ttn');
var appEUI = '70B3D57ED000033E';
var accessKey = '********************************************';
var client = new ttn.Client('staging.thethingsnetwork.org', appEUI, accessKey);
client.on('uplink', function (msg) {
console.log('Received message', msg);
});
client.on('activation', function (msg) {
console.log('Device activated:', msg.devEUI);
});

## Slide 37: TTN Fair Use Policy
Golden rule: 30 seconds air-time per device per day
For 10 bytes of payload, this translates in (approx.):
  20 messages per day at SF12
  500 messages per day at SF7
This allows for >1000 nodes per gateway

## Slide 38: Freifunk & TTN
Create an IoT network like LoRaWAN available to everyone everywhere
Own. The. Network.
Create a “canvas” Let’s play!
Open Data by default
Freifunk as Backhaul Network

## Slide 39: Bootstrap Münster
Notes: Stumbled across LPWAN via SIGFOX
“I want this for everyone, without the NDA & license fee and as a community thing inside Freifunk”
Found TTN, build first gateway
Silly idea: „wiekaltistderkanal.de“
Done
Learned a lot. \o\ \o/ /o/

## Slide 40: wiekaltistderkanal.de
wiekaltistderkanal.de

## Slide 42: STOLEN!

## Slide 43: We're back!

## Slide 44: Demo.
wiekaltistderkanal.de
Open Data on https://opensensemap.org.

## Slide 45: Things we're working on
Detect & publish occupied e-car charging spots
Local river: Water level measurements (Use: Flood thread detection)
Misc. environmental sensors, together with sensebox.de

## Slide 46: Summary: Living with Restrictions
Respect the Fair Use Policy!
Do not bend the rules - Rethink use cases.
How low can you go*?
*Look at TPL5110. 35nA

## Slide 47: Links
Münster
  wiekaltistderkanal.de
  Forum Münsterland: https://forum.freifunk-muensterland.de/c/ffms-lp
Sensebox
  Solar Prototyp: https://opensensemap.org/explore/57fb712811347b0011c10e80
The Things Network
  https://www.thethingsnetwork.org
  https://www.thethingsnetwork.org/wiki/Home
  https://www.thethingsnetwork.org/forum/

## Slide 48
vax@kgbvax.net
@kgbvax